## Slide 1: CSE 3124 : Computer Networks [2 1 0 3]

## Slide 2: Module 1: Computer Networks & the Internet
Introduction
our goal:
•
•
get “feel” and terminology
more depth, detail
later in course
approach:
– use Internet as example
•
•
•
•
•
•
•
overview:
what’s the Internet? what’s a protocol?
Network edge; Hosts, Access net, Physical media
Network core: Packet/Circuit switching, Internet structure Performance: Loss, Delay,
Throughput
Protocol layers, Service Models
History

## Slide 3
A computer network is a group of interconnected devices (such as computers, servers, and routers) that communicate and share resources using wired or wireless connections.
These networks allow data exchange, collaboration, and access to shared resources like printers, files, and the internet.
Computer Network
Notes: 3

## Slide 4: Networking = “Plumbing”
Networking is the “plumbing” of computing
Almost all areas of computing are network-based.
  Distributed computing
  Big Data
  Cloud Computing
  Internet of Things
  Smart Cities
Networking is the backbone of computing.

## Slide 5: Internet Age
Distributed Computing
Cloud Computing
Mobile Computing ⇒ Smart Phones
Streaming Video ⇒ YouTube
Social Networking ⇒ FaceBook
Big Data
Machine Learning ⇒ Artificial Intelligence
Online Shopping ⇒ Amazon, eBay
Most fields today – Education, Health, Environment – are advancing simply because of advances in networking.

## Slide 6: Current Hot Topics in Networking
Internet of Things (IoT)
Cybersecurity
Cloud Computing
Software Defined Networking
Wireless Networking
Streaming Media

## Slide 7
Trend: Smart Everything |  | 
Smart Watch | Smart TV | Smart Car
Smart Health | Smart Home | Smart Kegs
Smart Space | Smart Industries | Smart Cities

## Slide 8
Trend: Smart to Intelligent |  |  | 
Intelligent Clock | Intelligent TV | Intelligent Car | 
Intelligent Health | Intelligent Home Security | Intelligent Microwave | 
Intelligent Light | Amazon Alexa | Google Assistant | 

## Slide 9: Trend: Security & Cyber Warfare
Security of computers, companies, smart grid, and nations
Nation States are penetrating other nations’ computers 5th domain of warfare (after land, sea, air, space)
In 2010, the US set up US Cyber Command
UK, China, Russia, Israel, and North Korea have similar centers
Many cyber wars: North Korea vs. USA, Israel vs. Syria, South Korea vs. North Korea, India vs. Pakistan, …
New
Old

## Slide 10: What’s the Internet: “nuts and bolts” view
millions of connected computing devices:
–
–
hosts = end systems
running network apps

fiber, copper, radio, satellite transmission rate: bandwidth
wireless communication links
 Packet switches: forward packets (chunks of data)
routers and switches
wired
links
links
router
mobile network
global ISP
home network
regional ISP
institutional
network
wireless laptop
smartphone
PC
server
Introduction

## Slide 11: “Fun” internet appliances
IP picture frame http://www.ceiva.com/
Web-enabled toaster + weather forecaster
Internet phones
Slingbox: watch,
control cable TV remotely
Internet refrigerator
Tweet-a-watt: monitor energy use
Introduction

## Slide 12: What’s the Internet: “nuts and bolts” view
•
Internet: “network of networks”
Interconnected ISPs
protocols control sending, receiving of msgs
e.g., TCP, IP, HTTP, Skype, 802.11
Internet standards
RFC: Request for comments
IETF: Internet Engineering Task Force
•
•
mobile network
global ISP
regional ISP
home network
institutional
network

## Slide 13: What’s the Internet: a service view
•
Infrastructure that provides services to applications:
– Web, VoIP, email, games, e-commerce, social nets, …
provides programming interface to apps
•
mobile network
global ISP
regional ISP
home network
institutional
network

## Slide 14: A closer look at network structure:
 network edge: applications and hosts
 network core:
 routers
 network of networks
 access networks, physical media: communication links

## Slide 15: The network edge:
 end systems (hosts):
 run application programs
 e.g. Web, email
 at “edge of network”

## Slide 16: The network edge:
 client/server model
 client host requests, receives service from always-on server
 e.g. Web browser/server; email client/server
 why such a popular model?

## Slide 17: The network edge:
 peer-peer model:

minimal (or no) use of
dedicated servers
 e.g. Gnutella, KaZaA
 SETI@home?

## Slide 18: What’s a protocol?
human protocols:
 “what’s the time?”
 “I have a question”
 introductions
network protocols:
 machines rather than humans
 all communication activity in Internet governed by protocols
protocols define format, order of msgs sent and received among network entities, and actions taken on msg
transmission, receipt

## Slide 19: What’s a protocol?
a human protocol and a computer network protocol:
Q: Why are protocols so important?
Hi
Hi
Got the time? 2:00
TCP connection req
TCP connection response
Get http://www.awl.com/kurose-ross
<file>
time

## Slide 20: Internet Services Models
 Connection-oriented service
 Connectionless service
 Applications
 FTP, Internet Phone, Web, Internet radio, email

## Slide 21: Connection-oriented service
Introduction
1-14
 Goal: data transfer between end systems
 handshaking: setup (prepare for) data transfer ahead of time
 TCP - Transmission Control Protocol
 Internet’s connection-oriented service
 reliable, in-order byte-stream data transfer
loss: acknowledgements and retransmissions
 flow control:
sender won’t overwhelm receiver
 congestion control:
senders “slow down sending rate” when network
congested

## Slide 22: Connectionless service
Goal: data transfer between end systems
 same as before!
 UDP - User Datagram Protocol [RFC 768]:
connectionless
unreliable data transfer
no flow control
no congestion control
What’s it good for?

## Slide 23: A Comparison
App’s using TCP:
 HTTP (Web), FTP (file transfer), Telnet (remote login), SMTP (email)
App’s using UDP:
 streaming media, teleconferencing, DNS, Internet telephony

## Slide 24: The Network Core
 mesh of interconnected routers
 the fundamental question: how is data transferred through net?
 circuit switching: dedicated circuit per call: telephone net
 packet-switching: data sent thru net in discrete “chunks”

## Slide 25: Network Core: Circuit Switching
End-end resources reserved for “call”
 link bandwidth, switch capacity
 dedicated resources: no sharing
 circuit-like (guaranteed) performance
 call setup required
 must divide link bw into pieces...

## Slide 26: Circuit Switching: FDM and TDM
FDM
frequency
time
TDM
frequency
time
4 users
Example:

## Slide 27: Circuit Switching: FDM and TDM
TDM (Time Division Multiplexing) and FDM (Frequency Division Multiplexing) both are multiplexing techniques where TDM is used in both analogue and digital signals.
Where as FDM used only in analogue signals.

## Slide 28: Network Core: Packet Switching
each end-end data stream divided into packets
 user A, B packets share network resources
 each packet uses full link bandwidth
 resources used as needed
resource contention:
 aggregate resource demand can exceed amount available
 what happens if bandwidth is not available?
 congestion: packets queue, wait for link use
 store and forward: packets move one hop at a time

Node receives complete packet before forwarding

## Slide 29: Packet Switching: Statistical Multiplexing
Sequence of A & B packets does not have fixed pattern  statistical multiplexing.
A
B
C
10 Mb/s
Ethernet
1.5 Mb/s
D
E
statistical multiplexing
queue of packets waiting for output link

## Slide 30: Packet Switching: Statistical Multiplexing
In statistical multiplexing, packets from sources A and B are sent based on demand.
The sequence of packets (A, B, A, A, B, etc.) does not follow a fixed pattern—this is what makes it statistical.

## Slide 31: Packet switching versus circuit switching
 circuit-switching:
 10 users
 packet switching:
 with 35 users, probability > 10 active less than .0004
Packet switching allows more users to use network!
 1 Mb/s link
 each user:
 100 kb/s when “active”
 active 10% of time
N users
1 Mbps link

## Slide 32: Packet switching versus circuit switching
Is packet switching a “slam dunk winner?”
 Great for bursty data
 resource sharing
 simpler, no call setup
 Excessive congestion: packet delay and loss
 protocols needed for reliable data transfer, congestion control
 Circuit Switching = Guaranteed behavior
 good for which apps?

## Slide 33: Packet-switching: store-and-forward
 Entire packet must arrive at router before it can be transmitted on next link: store and forward
 delay = 3L/R
R
 Takes L/R seconds to transmit (push out) packet of L bits on to link or R bps
R
R
Example:
 L = 7.5 Mbits
 R = 1.5 Mbps
 delay = 15 sec
L

## Slide 34: Packet-switched networks: forwarding
 Goal: move packets through routers from source to destination
 we’ll study several path selection (i.e. routing) algorithms (chapter 4)
 datagram network:
 destination address in packet determines next hop
 routes may change during session
 analogy: driving, asking directions
 virtual circuit network:
 each packet carries tag (virtual circuit ID), tag determines next hop
 fixed path determined at call setup time, remains fixed thru call
 routers maintain per-call state

## Slide 35: Network Taxonomy
Telecommunication networks
Circuit-switched networks
FDM
TDM
Packet-switched networks
Networks with VCs
Datagram Networks
Datagram network is not either connection-oriented or connectionless.
Internet provides both connection-oriented (TCP) and connectionless services (UDP) to apps.

## Slide 36: Access networks and physical media
Q: How to connect end systems to edge router?
 residential access nets
 institutional access networks (school, company)
 mobile access networks
Keep in mind:
 bandwidth (bits per second) of access network?
 shared or dedicated?

## Slide 37: Residential access: point to point access
 Dialup via modem
 up to 56Kbps direct access to router (often less)
 Can’t surf and phone at same time: can’t be “always on”
 ADSL: asymmetric digital subscriber line
 up to 1 Mbps upstream (today typically < 256 kbps)
 up to 8 Mbps downstream (today typically < 1 Mbps)
 FDM: 50 kHz - 1 MHz for downstream
4 kHz - 50 kHz for upstream
0 kHz - 4 kHz for ordinary telephone

## Slide 38: Residential access: cable modems
 HFC: hybrid fiber coax
 asymmetric: up to 30Mbps downstream, 2 Mbps upstream
 network of cable and fiber attaches homes to ISP router
 homes share access to router
 deployment: available via cable TV companies

## Slide 39: Cable Network Architecture: Overview
Typically 500 to 5,000 homes
cable headend
home
cable distribution network (simplified)

## Slide 40: Cable Network Architecture: Overview
cable headend
home
cable distribution network (simplified)

## Slide 41: Company access: local area networks
 company/univ local area network (LAN) connects end system to edge router
 Ethernet:
 shared or dedicated link connects end system and router
 10 Mbps, 100Mbps, Gigabit Ethernet
 LANs: chapter 5

## Slide 42: Wireless access networks
 shared wireless access network connects end system to router
 via base station aka “access point”
 wireless LANs:
 802.11b (WiFi): 11 Mbps
 wider-area wireless access
 provided by telco operator
 3G ~ 384 kbps
Will it happen??
 WAP/GPRS in Europe
router
base station
mobile hosts

## Slide 43: Home networks
Typical home network components:
 ADSL or cable modem
 router/firewall/NAT
 Ethernet
 wireless access point
wireless access point
wireless laptops
router/ firewall
cable modem
to/from cable headend
Ethernet

## Slide 44: Physical Media
 Bit: propagates between transmitter/rcvr pairs
 physical link: what lies between transmitter & receiver
 guided media:
 signals propagate in solid media: copper, fiber, coax
 unguided media:
 signals propagate freely, e.g., radio
Twisted Pair (TP)
 two insulated copper wires
 Category 3: traditional phone wires, 10 Mbps Ethernet
 Category 5: 100Mbps Ethernet

## Slide 45: Physical Media: coax, fiber
Coaxial cable:
 two concentric copper conductors
 bidirectional
 baseband:
 single channel on cable
 legacy Ethernet
 broadband:

multiple channel on cable HFC

Fiber optic cable:
 glass fiber carrying light pulses, each pulse a bit
 high-speed operation:
 high-speed point-to-point transmission (e.g., 5 Gps)
 low error rate: repeaters spaced far apart ; immune to electromagnetic noise

## Slide 46: Physical Media: coax, fiber
Feature | Fiber Optic Cable | Copper Coaxial Cable
Speed / Bandwidth | Much higher bandwidth (10 Gbps and beyond) | Lower bandwidth; suitable for limited-speed usage
Distance | Transmits over longer distances without signal loss | Signal degrades faster, needs frequent amplifiers
Interference | Immune to electromagnetic interference | Susceptible to EMI and radio frequency interference
Signal Quality | Very low loss and high-quality signal | More signal attenuation over distance
Security | Difficult to tap without detection (more secure) | Easier to tap into (less secure)
Size and Weight | Lighter and thinner | Thicker and heavier
Cost (initial) | Higher installation cost | Cheaper initially

## Slide 47: Electromagnetic Spectrum
 signal carried in electromagnetic spectrum
 no physical “wire”
 bidirectional
 propagation environment effects:
 reflection
 obstruction by objects
 interference
Radio link types:
 terrestrial microwave
 e.g. up to 45 Mbps channels
 LAN (e.g., Wifi)
 2Mbps, 11Mbps
 wide-area (e.g., cellular)
 e.g. 3G: hundreds of kbps
 satellite
 up to 50Mbps channel (or multiple smaller channels)
 270 msec end-end delay
 geosynchronous versus low altitude

## Slide 48: Physical media: radio
 signal carried in electromagnetic spectrum
 no physical “wire”
 bidirectional
 propagation environment effects:
 reflection
 obstruction by objects
 interference
Radio link types:
 terrestrial microwave
 e.g. up to 45 Mbps channels
 LAN (e.g., Wifi)
 2Mbps, 11Mbps
 wide-area (e.g., cellular)
 e.g. 3G: hundreds of kbps
 satellite
 up to 50Mbps channel (or multiple smaller channels)
 270 msec end-end delay
 geosynchronous versus low altitude

## Slide 49: Internet structure: network of networks
Introduction
1-41
 “Tier-3” ISPs and local ISPs
 last hop (“access”) network (closest to end systems)
NAP
Tier-2 ISP
local ISP
local ISP
local ISP
local ISP
Tier 3 ISP
Tier-2 ISP
local ISP
Tier-2 ISP
local ISP
Tier-2 ISP local ISP
Tier-2 ISP
local ISP
Local and tier- 3 ISPs are customers of higher tier ISPs
connecting them to rest of Internet

## Slide 50: ISP: e.g., Sprint
Sprint US backbone network

## Slide 51: Internet structure: network of networks
1-42
 a packet passes through many networks!
NAP
Tier-2 ISP
Tier 3 ISP
Tier-2 ISP
local ISP
local ISP
local ISP
local ISP
local ISP
Tier-2 ISP local ISP
Tier-2 ISP
local ISP

## Slide 52: How do loss and delay occur?
Introduction
1-43
B
packets queue in router buffers
 packet arrival rate to link exceeds output link capacity
 packets queue, wait for turn
packet being transmitted (delay)
A
packets queueing (delay)
free (available) buffers: arriving packets dropped (loss) if no free buffers

## Slide 53: Four sources of packet delay
Introduction
1-44
 1. nodal processing:
 check bit errors
 determine output link
A
B
propagation
transmission
nodal processing
queueing
 2. queueing
 time waiting at output link for transmission
 depends on congestion level of router

## Slide 54: Delay in packet-switched networks
Introduction
1-45
3. Transmission delay:
 R=link bandwidth (bps)
 L=packet length (bits)
 time to send bits into link = L/R
4. Propagation delay:
 d = length of physical link
 s = propagation speed in medium (~2x108 m/sec)
 propagation delay = d/s
A
B
propagation
transmission
nodal processing
queueing
Note: s and R are very
different quantities!

## Slide 55: Nodal delay
dnodal =dproc +dqueue +dtrans +dprop
 dproc = processing delay
 typically a few microsecs or less
 dqueue = queuing delay
 depends on congestion
 dtrans = transmission delay
 = L/R, significant for low-speed links
 dprop = propagation delay
 a few microsecs to hundreds of msecs

## Slide 56: Packet loss
 queue (aka buffer) preceding link in buffer has finite capacity
 when packet arrives to full queue, packet is dropped (aka lost)
 lost packet may be retransmitted by previous node, by source end system, or not retransmitted at all

## Slide 57: Network System Modularity
Like software modularity, but:
Implementation is distributed across many machines (routers and hosts)
Must decide:
  How to break system into modules
    Layering
  Where modules are implemented
    End-to-End Principle
  Where state is stored
    Fate-sharing

## Slide 58: Network System Modularity
Like software modularity, but:
Implementation is distributed across many machines (routers and hosts)
Must decide:
  How to break system into modules
    Layering
  Where modules are implemented
    End-to-End Principle
  Where state is stored
    Fate-sharing

## Slide 59: Layering Concept
A restricted form of abstraction: system functions are divided into layers, one built upon another
Often called a stack; but not a data structure!

## Slide 60: Layers and Communications
Interaction only between adjacent layers
layer n uses services provided by layer n-1
layer n provides service to layer n+1
Bottom layer is physical media
Top layer is application

## Slide 61: Entities and Peers
Entity – a thing (an independent existence) Entities interact with the layers above and below Entities communicate with peer entities
– same level but different place (eg different person, different box, different host)
Communications between peers is supported by entities at the lower layers

## Slide 62: Entities and Peers
Entities usually do something useful
Encryption – Error correction – Reliable Delivery
Nothing at all is also reasonable
Not all communications is end-to-end Examples for things in the middle
IP Router – Mobile Phone Cell Tower
Person translating French to English

## Slide 63: Protocol “Layers”
Networks are complex!
 many “pieces”:
 hosts
 routers
 links of various media
 applications
 protocols
 hardware,
software

## Slide 64: Organization of air travel
 a series of steps
ticket (purchase)
baggage (check) gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload) runway landing airplane routing
airplane routing

## Slide 65: Layering of airline functionality
ticket (purchase)
baggage (check)
gates (load)
runway (takeoff)
airplane routing
departure airport
arrival airport
airplane routing airplane routing
intermediate air-traffic control centers
ticket (complain)
baggage (claim
gates (unload)
runway (land)
airplane routing
ticket
baggage gate
takeoff/landing
airplane routing
Layers: each layer implements a service
 via its own internal-layer actions
 relying on services provided by layer below

## Slide 66: Why layering?
Layering is a design approach that divides the complex process of communication into simpler, well-defined steps (layers), where each layer performs a specific task.

## Slide 67: Internet protocol stack
 | application
 | transport
 | network
 | link
 | physical

application: supporting network applications

ftp, smtp, http

transport: host-host data transfer

tcp, udp

network: routing of datagrams from source to destination

ip, routing protocols

link: data transfer between neighboring network elements

ppp, ethernet

physical: bits “on the wire”, modulation scheme, line-coding format, electrical & physical specifications, etc.
Routers in the network operate only up to the Network Layer

Host
Router

## Slide 68: source
Introduction
1-59
message
segment
datagram frame
application
transport
network
link
physical
Hl | Hn | Ht | M
Hn | Ht | M
Ht
M
M
destination
application
transport
network
link
physical
Hl | Hn | Ht | M
Hn | Ht | M
Ht
M
M
network
link
physical
link
physical
Hl | Hn | Ht | M
Hn | Ht | M
Hl | Hn | Ht | M
Hn | Ht | M
Hl | Hn | Ht | M
Hl | Hn | Ht | M
router
switch
Encapsulation

## Slide 69: 1.9 Internet History
1961: Kleinrock - queueing theory shows effectiveness of packet- switching
1964: Baran - packet- switching in military nets
1967: ARPAnet conceived by Advanced Research Projects Agency
1969: first ARPAnet node operational
 



1972:
 ARPAnet demonstrated publicly
 NCP (Network Control Protocol) first host- host protocol
 first e-mail program
 ARPAnet has 15 nodes
1961-1972: Early packet-switching principles

## Slide 70: Internet History

1970: ALOHAnet satellite network in Hawaii
1973: Metcalfe’s PhD thesis proposes Ethernet
1974: Cerf and Kahn - architecture for interconnecting networks
late70’s: proprietary architectures: DECnet, SNA, XNA
late 70’s: switching fixed length packets (ATM precursor)
1979: ARPAnet has 200 nodes





Cerf and Kahn’s internetworking principles:
 minimalism, autonomy - no internal changes required to interconnect networks
 best effort service model
 stateless routers
 decentralized control define today’s Internet
architecture
1972-1980: Internetworking, new and proprietary nets

## Slide 71: Internet History
 1983: deployment of TCP/IP
 1982: smtp e-mail protocol defined
 1983: DNS defined for name-to-IP-address translation
 1985: ftp protocol defined
 1988: TCP congestion control
 new national networks: Csnet, BITnet, NSFnet, Minitel
 100,000 hosts connected to confederation of networks
1980-1990: new protocols, a proliferation of networks

## Slide 72: Internet History

Early 1990’s: ARPAnet decommissioned
1991: NSF lifts restrictions on commercial use of NSFnet (decommissioned, 1995)
early 1990s: WWW
 hypertext [Bush 1945, Nelson 1960’s]
 HTML, http: Berners-Lee
 1994: Mosaic, later Netscape
 late 1990’s: commercialization of the WWW


Late 1990’s & 2000’s:

est. 50 million computers on Internet
est. 100 million+ users
backbone links running at 1 Gbps


1990’s: commercialization, the WWW
You now hopefully have:

context, overview, “feel” of networking
more depth, detail later in course
